## Slide 1: Mitigating a SYN flood DDoS attack in a software defined network
Damien McGloin - 40000631

## Slide 2: Introduction and background

## Slide 3: Introduction and background
Typically, the first step is implementing preventative measures before an attack has taken place.
This could include firewall measures or the process of hardening e.g changing default passwords.
However, this project will focus on the detection and mitigation of an attack.

## Slide 4: What is a SYN flood attack?
This is a type of DoS/DDoS attack.
It's a layer 4 (transport layer) targeting the TCP protocol
It violates the TCP protocol's three way handshake.

## Slide 5: What is a SYN flood attack?
Typically an attacker will spoof their ip address and send SYN packets to every port of the targeted server.
The server will respond to each attempt with a SYN-ACK packet from each open port.
However, if the ip address is spoofed the attacker won't receive the SYN-ACK packets and the target also won't receive an ACK packet.
Therefore, the connection will remain open.

## Slide 6: What is a SYN flood attack?
Once the server's connection overflow tables have filled service to legitimate clients will stop and the server may crash

## Slide 7: Example of Syn flood DDoS attack

## Slide 8: Example of Syn flood DDoS attack

## Slide 9: Availability
We live in a society heavily dependent on online services.
This includes hospitals, food supply chains and financial institutions.
A SYN flood attack as described poses a threat to the security goal of availability. Part of the CIA triad (Confidentiality, Integrity, Availability).
It would be classified as sabotage of available services or systems.
The application created for this project is designed as a countermeasure against this.

## Slide 10: Explanation and justification of design choices

## Slide 11: Approach
The first step in the project is identifying an attack.
This can be done by assessing traffic on the network.
It will be assumed for the purpose of this project that the attackers will be using spoofed ip addresses.

## Slide 12: Distinguishing between legitimate and malicious traffic

## Slide 13: Distinguishing between legitimate and malicious traffic

## Slide 14: Tools used
SDN cockpit.
The hping3 tool will be used for generating traffic both malicious and otherwise.
The mininet virtual network emulator will be used within SDN cockpit to configure a network topology.
A ryu openflow controller (v1.3) will be used to implement the solution for monitoring and preventing the attack.
Wireshark will be used for monitoring and demonstration purposes.
Xterm will be used to emulate terminal windows for various hosts.
iPerf will be used for measuring bandwidth on the network.

## Slide 15: Detection
By implementing a traffic monitor my application will be able to assess the number of packets transmitted.
This information will be stored every ten seconds and compared against previous stored information.
This means if the application is running for hours it will still be able to detect a recent spike in traffic.

## Slide 16: Gathering data
After this TCP traffic will be directed to the controller.
This will add latency but allow the application to gather data.
The ip addresses of each user will be stored along with the number of SYN packets they have sent and ACK packets they have received.
This will determine whether they are a legitimate user or an attacker using a spoofed ip address.

## Slide 17: Mitigating the attack
At this stage a drop rule will be created for these users.
Packets which have not been dropped will be processed by the controller temporarily preventing any traffic from being sent on the network.
After the controller finishes processing these packets legitimate traffic can be sent thus preserving availability on the network.

## Slide 18: Network Topology Diagram

## Slide 19: Results and Evaluation

## Slide 20: Functional Evaluation

## Slide 21: Evaluation
In terms of functionality the application performs as it was designed to.
It correctly monitors the network, detects high volumes of traffic sent within a short span of time, redirects TCP traffic to the controller and then collects data on each IP address.
After assessing the ip addresses block rules are put in place for any users considered to be malicious.
Testing repeatedly has shown that the time between the traffic monitor redirecting traffic can vary though based on the imprecise method used to detect a spike in traffic within a short period of time.
The application's ability to block users becomes less effective as the number of hosts launching attack traffic increases.

## Slide 22: Non-Functional Testing

## Slide 23: Evaluation
As shown through testing the effectiveness of the application depends heavily on two factors.
1. The speed of the packets sent by an attacker
2. The number of hosts attacking the system
Sending packets at 100 per second led to a generally small percentage not being dropped
The highest in this instance was 1.67% of the total packets sent
Using the flood mode of the hping3 tool the drop rate became generally higher but this was not consistent throughout testing
The highest drop rate was 17.78% when six hosts were attacking but with seven hosts attacking this was much lower. Only 3.84%
This suggests the application can not reliably block high speed malicious traffic

## Slide 25: Evaluation
It also must be noted that during test 4.4, in which seven hosts launched a SYN flood attack against one target, the application was unable to create block rules for all seven attackers and a large amount of malicious traffic was not dropped as a result.
Later in test 4.9 the application succeeded in blocking seven attackers. This failing may have been an anomaly but further indicates the limitations of the application.
It is likely that generating too many flow rules would severely limit the effectiveness of the solution
The duration of the attack must be noted as well.
Using the hping3 attack tool's flood mode this duration ranged from a low of 38 seconds with one attacker to a high of 675 seconds with six attackers.
The time to set up the attack should also be considered which increases based on the number of hosts launching an attack.
However, this does highlight that the more attackers there are on the system the slower it is at stopping an attack.

## Slide 27: Conclusion

## Slide 28: Conclusion
While the application has been shown to successfully block traffic from up to seven hosts there are serious limitations as well.
The possibility of too many flow rules overwhelming the system, the number of packets not being blocked when there are multiple attackers and and the increasing time period in which the controller must process packets which were not blocked.
These failings of the application highlight the benefits of a second approach in which the application does not target the attacker but instead targets the destination.
Blocking SYN traffic from reaching the destination would affect availability and in a sense does the attacker's job for them.
However, the advantages may outweigh the disadvantages.
With a longer timeline for this project the next step would be creating this kind of alternate solution.